## Slide 1: Advertisement And Signs Ordinance Seminar
Amendment To Chapter 4 of the Detroit City Code
Notes: All font should be Montserrat
Text within content blocks should be 12pt font
To edit Department in the lower right corner, click Slide, Edit Master. In top “Master” slide edit Department name in footer

## Slide 2: SESSION OVERVIEW AND HIGHLIGHTS
SESSION #4
TITLE: BUSINESS SIGNS, CONSTRUCTION INSPECTIONS, LICENSE & MAINTENANCE
Session Time: Approximately 1.5 hours
Overview: Overview of general requirements and review major changes impacting business sign. Overview of construction inspections, Certificate of Acceptance. Outline sign license, maintenance requirements and enforcement. Overview of MDOT requirements for regulated roads.

## Slide 3: BUSINESS SIGNS REQUIRMETNS AND PROCESS
Presenter: Eric B. Johnson
Supervising Building Inspector
Developer Resource Center (DRC)
Building Safety Engineering And Environmental Department

## Slide 4: BUSINESS sign requirements
DEFINITION:
BUSINESS SIGN means a sign containing a commercial message that is intended to direct attention to a principal business or principal commodity, service, or entertainment that is conducted, sold, or offered on the premises on which the sign is located, or if the sign is located in the right-of-way then on the premises adjacent to the location of the sign. at a scale and intensity that is reasonably proportional to the degree of physical presence or economic activity of the business, commodity, service, or entertainment at such premises. Identification signs and sponsorship signs are types of business signs.
Sec. 4-4-17 Sign erection or alteration to require new permit, sign operation or maintenance to require license It shall be unlawful to post. construct, erect, or otherwise display a sign without having first been issued a permit for such sign. It shall be unlawful to operate or maintain a sign without having first been issued a license for such operation. The term of any such license shall not exceed two years.
Sec. 4-4-21. Amortization. (a) Any sign for which a permit, grant, or other approval has been issued prior to the effective date of this ordinance. that is in compliance with all terms and conditions of such approval. but that does not conform to the provisions and standards of Chapter 4, Article 4. Divisions 2 through 7. shall not be subject to the dimensional standards and other substantive requirements of this Article until January 1, 2030.
Sec. 4-4-22. Waivers and adjustments to sign standards. (a) Any dimensional or operational standard or requirement set forth in this article may be subject to waiver or adjustment in accordance with the provisions of this section, except as expressly limited or prohibited.

## Slide 5: BUSINESS sign requirements (cont’d)
Sec. 4-4-23. Appeals of administrative decisions under this chapter. (a) In accordance with Chapter 3. of this Code, Administrative Hearings and Enforcement. and Administrative Appeals, Division IV, Administrative Appeals, as well as the rules of procedure promulgated thereunder, any appeal of an administrative decision made pursuant to Section 4-4-22 of this Code shall be made to the Department of Appeals and Hearings.
Sec. 4-4-35. Dynamic signs. (a) Permissibility. (I) Dynamic signs are permissible only in low-density commercial/ institutional sign districts and high-density commercial/industrial sign districts. Dynamic signs may be animated only in the Central Business District.
Sec. 4-4-36. Illuminated signs. (a) Permissibility. Illuminated signs are permissible in all sign districts. Illuminated signs in low-density residential sign districts may be externally illuminated only.
Sec. 4-4-41. Portable signs. (a) Permissibility. Portable signs are permissible in all sign districts. except that portable signs in low-density residential sign districts are permissible only as temporary signs. The permissibility of portable signs located in a public right-of-way is further subject to approval by the Department of Public Works, or other public agency with jurisdiction over such right-of-way.

## Slide 6: BUSINESS sign requirements (cont’d)
Sec. 4-4-62. Limitation on maximum aggregate business sign area. For any premises in a low-density residential sign district that contains a single-family, two-family, or multi-family residential building or structure with not more than four dwelling units, six square feet. For any premises in a low-density residential sign district that is not identified in Subsection (a)(l) of this section, and in any high-density residential/mixed use sign district, low-density commercial/institutional sign district. or recreation/open space sign district, the greater of: a. 2.6 square feet per linear foot of building frontage, not to exceed 500 square feet; or b. One square foot per linear foot of premises frontage, not to exceed 500 square feet. In any high-density commercial/industrial sign district, three square feet per linear foot of building frontage, provided that the maximum permissible aggregate area in any such district located outside the Central Business District, shall not exceed . 500 square feet.
For any corner premises that fronts onto a freeway, major thoroughfare, or secondary thoroughfare. the maximum permissible aggregate area as determined in Subsection (a) of this section shall be calculated, and shall apply, separately for each frontage of the premises. For any comer premises that does not front onto a freeway, major thoroughfare, or secondary thoroughfare, the maximum permissible aggregate area for the entire premises as determined in Subsection (a) of this section shall be calculated based only on the longest frontage of the premises.

## Slide 7: BUSINESS sign requirements (cont’d)
Sec. 4-4-63. Additional aggregate business sign area allowances. (a) Notwithstanding the aggregate business sign area limits set forth in Section 4-4-62 of this Code, additional aggregate area for business signs is permissible m the following circumstances and subject to the following limits:
  (1) High-rise identification signs. On any building or structure located within the Central Business District that does not contain a roof sign and for which the height of the roofline or parapet exceeds I 00 feet, not more than two high-rise
identification signs are permissible, subject to the following:
  The minimum clearance of each sign must be 100 feet;
  The maximum area of any sign is determined by its clearance and the linear width of the building facade to which the sign is affixed, measured at the height of the sign, as follows:

## Slide 8: BUSINESS sign requirements (cont’d)
For any sign with a clearance of at least 100 feet but less than 200 feet, the area of the sign must not exceed two square feet per linear foot of building width; For any sign with a clearance of at least 200 feet but less than 300 feet, the area of the sign must not exceed three square feet per linear foot of building width; or (iii) For any sign with a clearance of at least 300 feet, the area of the sign must not exceed four square feet per linear foot of building width; Not more than one high-rise identification sign may be located on any facade of a building or structure; Not more than two high-rise signs may be located on any premises: and Any high-rise identification sign may be illuminated, either internally or externally, but may not be dynamic.
Painted side-wall signs. On any building or structure that is not more than two stories and that is adjacent to a surface parking lot or other property that does not contain a permanent building or structure, such that the side facade of the building is exposed, not more than one sign is permissible on such side wall, subject to the following:
The sign must be a painted sign;
The sign may be either non-illuminated or illuminated externally;
The height of the sign must not exceed the height of the first story of the building or structure; and
The area of the sign must not exceed 500 square feet, excluding the area of any windows, doors, or other openings in the facade.

## Slide 9: BUSINESS sign requirements (cont’d)
Sponsorship signs associated with public art. On any premises that contains a work of public art that is located on the exterior of the property, such as an art mural or sculpture, the cost of which is sponsored, not more than one sponsorship sign recognizing such sponsorship is permissible, subject to the following:
The sign must be located proximate to the work of public art;
The sign must be constructed as a wall sign or monument sign;
The height of the sign must not exceed the lesser of: half the height of the work of public art or 15 feet;
The sign may not be illuminated; and
The area of the sign may not exceed 5% of the area of the associated work of public art, but in no case more than 300 square feet. The area of the work of public art consisting of a mural or other two-dimensional form should be computed as if it is a sign, in accordance with Section 4-4-5 of this Code. The area of the work of public art consisting of a sculpture or other three dimensional form should be computed as the product of its height and one quarter of its perimeter at its base

## Slide 10: BUSINESS sign requirements (cont’d)
Sec. 4-4-64. Business signs on multi-tenant buildings and multi-building campuses. (a) On any premises containing a multi-tenant building or structure, the maximum aggregate business sign area for the premises as set forth in Section 4-4-62 of this Code, and any additional aggregate business sign allowances as set forth in Section 4-4-63 of this Code, may be allocated among the various tenants as may be determined by the building owner, or its agent, and each tenant, provided that such allocation is reasonably proportional to the relative degree of each tenant's physical occupation and economic activity at the premises.
(b) On any multi-building campus, the maximum aggregate business sign area for the premises as set forth in Section 4-4-62 of this Code, and any additional aggregate business sign allowances as set forth in Section 4-4-63 of this Code, may be allocated among the various buildings and open spaces within the campus as may be determined by the owner of the campus or its agent.
Secs. 4-4-67 - 4-4-80. Reserved. 15 SUBDIVISION B. ENTERTAINMENT DISTRICT
Sec. 4-4-84. Theater district; purpose and sign regulations.

## Slide 11: BUSINESS SIGNS REQUIREMENTS AND PROCESS
Q&A SESSION

## Slide 12: PERMIT INSPECTIONS & CERTIFICATE OF ACCEPTANCE PROCESS
Presenter: Randy Hargraves, Supervising Building Inspector
Construction Division
Buildings Safety Engineering and Environmental Department

## Slide 13: PERMIT INSPECTIONS & CERTIFICATE OF ACCEPTANCE PROCESS
Q&A SESSION

## Slide 14: PERMIT INSPECTIONS & CERTIFICATE OF ACCEPTANCE PROCESS
Presenter: Robert Watson, Supervising Building Inspector
Terry Martin, Supervising Building Inspector
Construction Division
Buildings Safety Engineering and Environmental Department

## Slide 15: PERMIT INSPECTIONS & CERTIFICATE OF ACCEPTANCE PROCESS
Q&A SESSION

## Slide 16: 2020 ADVERTISMENT AND SIGN ORDINANCE SEMINAR
CLOSING REMARKS
SESSION ADJOURNMENT