Voigt Park

795 Longfellow St

- Site Amenities:

      - Installation of all site amenities to be performed according to Manufacturer’s and standard GSD Specifications and Details. Tack weld hardware on all new site amenities for added security. Locations are to be verified by the City Representative prior to excavation and installation.

      - Provide and install four (2) benches, secured mounting on approximately 40 SF (4’ x 10’) gravel pad, at locations shown on the drawing.

- Trees - Wayne County (21-22 and 22-23):

      - Provide and install 18 trees at specified locations throughout the park. Installation for all trees to be performed as per GSD construction standards specifications, and details, and according to the supplier’s installation instructions. Location to be verified by City Representative prior to excavation and installation.

        - 3 – Acer saccharum, ‘Green Mountain’ Silver Maple - 2 ½” caliper min.

        - 2 – Picea pungens, Colorado Blue Spruce – 8’-12’ tall.

        - 11 – Ulmus, ‘Princeton’, Elm – 2 ½” caliper min.

        - 2 – Quercus bicolor, Swamp White Oak – 2 ½” caliper min.

- Site Restoration:

  - The completion of the site restoration work shall include, but is not limited to the restoration of all areas disturbed by the construction work operations such as:

    - backfilling, all final lawn rough grading, finish fine grading of the lawn surfaces as specified in the preparation to install the hydro-seeding materials for lawn areas, the actual hydro-seeding and fertilization of the prepared approved turf lawn areas, protection of all fixed site improvements like fencing, trees, play structures, walk and other paved surfaces from any over-spray, clean-up following installation work, aeration, and fertilizing, and other maintenance and care necessary to produce a quality lawn including scarifying and re-application of any bare areas as required until the new turf is fully established.

    - Confirm approval by City Representative and final clean-up of the Park to turn back over to the City, and all other items necessary to complete the job, whether specifically mentioned or implied. If the City Representative determines that top soil from this site or other project sites is acceptable topsoil the contractor may be allowed to reuse the acceptable topsoil as backfill material for site restoration.

- Mobilization:

  - Mobilization will be paid for on a contract lump sum basis.  Price paid shall be payment in full for all labor, material, and equipment necessary for all preparatory work and operations, including, but not limited to, those necessary for the movement of personnel, equipment, supplies, tools and any other incidentals that are required to project site; and any other facilities necessary to undertake the work on the project; and for other work and operations, which must be performed, or for expenses incurred, prior to beginning work on the various contract items at the project sites.  This item shall also include preconstruction costs, exclusive of bidding costs, which are necessary direct costs to the project and are of a general nature rather than directly attributable to other pay items under the contract. The price paid shall be payment in full for Mobilization throughout the progress of the project work until completed.

- Layout & Field Survey:

  - Layout and field survey will be contractor’s responsibility. Price shall be contractor’s responsibility to lay out all site elements, mark all field locations, set grades and review with City Representative for approval.

- Bonds & Insurance:

  - Contractor shall secure bonding and insurance required for this project, per General Conditions. Bonds and insurance shall be maintained for the duration of the project until closeout, final acceptance, and final payment.

- General Conditions:

  - General Conditions will be paid for at the Contract lump sum basis for work at all the various sites.  Price paid shall be payment in full for General Conditions items & work throughout the progress of the Project Work, until completed.

- Miscellaneous & Close-Out Work:

  - Price paid shall be payment in full for all submittals, testing, labor, material, layout and equipment necessary for the completion to the full satisfaction of the City of the work required by this Project not otherwise included in a pay item listed above, and for the preparation and submittal to the City of all manufacturer warranties, required test results, other miscellaneous required documents, final permit clearances, maintenance manuals and manufacturer data as may be required within individual specification sections of the Contract Documents, completion of any and all “punch list” work to satisfaction and acceptance of the City, “As Built” drawings given to the City Representative as a complete package and Final Waivers from all subcontractors and suppliers, release of Surety, and a final Sworn Statement.

- End of Scope of Work